MMDQ-codec (version 1)

(Min-Max-Differencies-Quantization Codec)

Sergei Mashkin
2015

Content

1. Overview
2. MMDQ-codec description
3. MATLAB simulation of MMDQ-codec
4. C-language implementation of MMDQ-codec
5. Comparing MMDQ with G.711 and G.726
6. Modem signal transparency of MMDQ and G.726 codecs

1.Overview

This document contains short description of Min-Max-Difference-Quantization (MMDQ) codec.

2.MMDQ-codec description

MMDQ-codec has been created as very low MIPS (i.e. very low CPU usage) alternative of G.726‑32 (ADPCM codec with 32 kbits/sec bitrate, 8000 Hz sample rate).

Main properties of MMDQ-codec:

- Very low MIPS (CPU usage)
- Waveform lossy compression
- No restoration delay after corrupter/lost received frame (Note: G.726 has this).
- Transparancy for fax (up to ???? bod) or DTMF signals (for bitrates >= 32 kbits/sec)
- Easy adaptation to other bitrates or/and sample rates
- Algorithm simplicity

2.1. Min-Max-Differencies-Quantization Frame Format

Note: MATLAB/Octave/FreeMat array index notation is used, so index of first array element is 1 (not 0)!

Encoded data frame has next format:

MINX/MAXX
MAXX/MINX
SMOOTH-BITS[2..S]
DIFF[1..(N-1)]

Where:

MINX - minimal signal value in signal frame to be encoded (it may be encoded by A-law/mu-law encoder or by other compander method)

MAXX - maximal signal value in signal frame to be encoded (it may be encoded by A-law/mu-law encoder or by other compander method)

Note: if MINX is first and MAXX is next, decoder must set SMOOTH-BIT[0]=0,
if MAXX is first and MINX is next decoder must set SMOOTH-BIT[0]=1.

S - total number of smooth bits.

SMOOTH-BITS[1..S] - array of smooth bits. Smooth bits define code of decoder function/table will be used to restore linear differencies from DIFF[] array elements.

N - number of signal samples in single frame to be encoded.

DIFF[1..(N-1)] - array of companded relative differencies between signal samples.

For example, 32 kbits/sec version of MMDQ-codec encoded data frame format is:

MINX (8 bits) - A-law companded signal value
MAXX (8 bits) - A-law companded signal value
SMOOTH-BITS (1 bit) - smooth bit number 2 (number 1 is defined by MIN/MAX order).
DIFF[1..13] (13*3=39 bits) - differencies (3 bits per difference, samples per frame is 14).

Total frame size (for 14 voice samples to be encoded) is 8+8+1+39=56 bits (7 bytes).

2.2.MMDQ Algorithm Description

Figure 1. MMDQ encode scheme

Note: MATLAB/Octave/FreeMat array index notation is used, so index of first array element is 1 (not 0)!

Encoding:

1. Get sound samples X[i], i=1..N in linear format (these may be decoded A-law).
2. Find MINX, MAXX over X[i], i=1..N
3. Calculate DIFFX=MAXX-MINX
4. Calculate DX[i]=X[i+1]-X[i], i=1..(N-1)
5. Get AMPDX = max(abs(DX[i])), i=1..(N-1) - maximum amplitude of DX[i].
6. For every difference companding function DV[s]=F[s](DX), s=1..SMOOTH_N calculate maximum reconstruction error ERR[s]:

6.1. Get DV[s][i]=F[s](DX[i]), i=1..(N-1)
Note: different companding functions F[s](DX) are used to minimize encode/decode reconstruction error.

Default F[s](DX) is linear function:
F[s](DX)=DX

6.2. Quantize DV[i] into DIFF[i] values. Here i=1..(N-1). If encoder use
        BITS bits per difference, then DIFF[i] will be of range [0..(FACTOR-1)],
        where FACTOR=2^BITS.
        Approximate quantization function is: DIFF[i]=FACTOR*DV[i]/AMPDX + FACTOR/2,
        where i=1..(N-1).

        Note special case: AMPDX==0

6.2. Prepare data_frame[s] for MINX, MAXX, SMOOTH==s, DIFF[s][i], i=1..(N-1)

        Note: if SMOOTH(bit0)==0, put MINX first, MAXX second.
        If SMOOTH(bit0)==1, put MAXX first, MINX second.

6.3. Decode data_frame[s] into sound waveform: Y[s][i], i=1..N

6.4. Calculate ERR[s]=max(abs(X[i]-Y[s][i])), i=1..N

7.Find MINERR=min(ERR[s]), s=1..SMOOTH_N. Let's s0 - SMOOTH for
data_frame with best (minimal) reconstruction error: ERR[s0]=MINERR.

8.Ouput data_frame[s0].

--------------------------------------------------------------------------------

Decoding:

1.Get encoded data: data_frame=B[k], k=1..M (M-total size of data, bits).

2.Get MINX, MAXX, SMOOTH_BIT[1..s], DIFF[1..(N-1)] from data_frame.
For example, for 32 kbits/sec 8000 Hz format:

M1=B[1..8]
M2=B[9..16]
if M1<=M2
    SMOOTH_BIT[1]=0
    MINX=M1
    MAXX=M2
else
    SMOOTH_BIT[1]=1
    MINX=M2
    MAXX=M1
end
SMOOTH_BIT[2]=B[17]
i=1
k=18
while(k<=M)
    DIFF[i]=B[k..k+2]
    i=i+1
    k=k+3
end

3.Calculate used smooth: s0=SMOOTH_BIT[1..s]

4.Calculate DIFFX=MAXX-MINXX

5.Calculate first estimation of sound samples values:
Y[1]=0
for i=2:N
    DY = R[s0]( 2*DIFF[i-1]/FACTOR - 1 )
    Y[i] = Y[i-1] + DY
end

Where DY=R[s](DIFF) is difference decompanding function for defined smooth s0.
This function is inverse for DIFF=F[s](DY).

6.Find MINY, MAXY over Y[i], i=1..N.

7.Calculate DIFFY=MAXY-MINY

8.Scale and shift Y[i], i=1..N to the range [MINX..MAXX] by formula:

for i=1:N
    Y[i] = DIFFX * ( Y[i]-MINY ) / DIFFY + MINX
end

Note special case: DIFFY==0

2.3.MMDQ Compand/Expand functions (smoothing)

MMDQ codec contains compand and expand functions. These functions let to minimize error of quantization. Default compand/expand functions are linear (ver0 on Figure 2-4). Some simulation in MATLAB leads me empirically to the next compand/expand combinations:

function y = compand( x , ver )
    switch ver
    case 0
        y = x;
    case 1
        y = sign(x) .* abs(x) .^ (1/1.25);
    case 2
        PWR = 1.35;
        N = length(x);
        y = zeros(1,N);
        for i=1:N
        if x(i)>=0 && x(i)<=0.5
        y(i) = 0.5*(2*x(i))^(1/PWR);
        elseif x(i)>0.5
        y(i) = 1-0.5*(2*(1-x(i)))^(1/PWR);
        elseif x(i)>=-0.5
        y(i) = -0.5*(2*(-x(i)))^(1/PWR);
        else
        y(i) = -1+0.5*(2*(1+x(i)))^(1/PWR);
        end
        end
    case 3
        y = sign(x) .* (1 - (1 - abs(x)) .^ (1/1.2));
    end
return

function y = expand( x , ver )
    switch ver
    case 0
        y = x;
    case 1
        y = sign(x) .* abs(x) .^ (1.25);
    case 2
        PWR = 1.35;
        N = length(x);
        y = zeros(1,N);
        for i=1:N
        if x(i)>=0 && x(i)<=0.5
        y(i) = 0.5*(2*x(i))^(PWR);
        elseif x(i)>0.5
        y(i) = 1-0.5*(2*(1-x(i)))^(PWR);
        elseif x(i)>=-0.5
        y(i) = -0.5*(2*(-x(i)))^(PWR);
        else
        y(i) = -1+0.5*(2*(1+x(i)))^(PWR);
        end
        end
    case 3
        y = sign(x) .* (1 - (1 - abs(x)) .^ (1.2));
    end
return

I think, that these functions is not the best. So, some investigations of this question is needed. May be this will be done in future versions of MMDQ-codec.

Figure 2. Compand functions

Figure 3. Expand functions

Figure 4. Compand (left) / Expand (right) functions (histogramms view). Ver0 – upper row, ver4 – bottom row.

3.MATLAB simulation of MMDQ-codec

MMDQ-codec has been implemented in MATLAB/Octave/FreeMat. All source code is available. There are two main implementations: floating point (CODEC_VERSION=1) and fixed point (CODEC_VERSION=2). Fixed point implementation works with precalculated tables for encoding and decoding and table for integer division. 16-bit, 32-bit and 64-bit integer arithmetics is used. Fixed point implementation was used as base code for C-language implementation. It has a (very) little lower quality than floating point variant.

Both implementations have been tested and some results are described below.

Next results have been generated with main_test.m script for female sample and CODEC_VERSION=1, bitrate=32 kbit/sec (SAMPLES_PER_FRAME=14, BITS_PER_SAMPLE=3), SMOOTH_ON=1.

Figure 5. Original and encoded/decoded female voice sample waveforms

Figure 6. Original and encoded/decoded female voice sample spectrograms

Figure 7. Original (x) and encoded/decoded (y) female voice sample waveform (quantized signal) and absolute errors (quantized signal error)

Figure 8. Original (x) and encoded/decoded (y) female voice sample waveform (quantized signal) and absolute errors (quantized signal error) near big error samples.

Figure 9. Text file with results of MMDQ-codec test for female sample.

Next table contains results for female, male, modem samples for both (floating-point and fixed-point) versions of MMDQ-codec (32 kbps/sec: spf=14, bps=3, smooth=4).

Table 1. Results of MMDQ-codec MATLAB simulation (compare floating point with fixed point implementation)
sample	Max normalized error		MSE
	Codec ver.1	Codec ver.2	Codec ver.1	Codec ver.2
female	0.12377930	0.12374878	0.00005001	0.00005006
male	0.13555908	0.13562012	0.00006900	0.00006883
modem	0.70791626	0.70791626	0.00540838	0.00540749

Figure 10. Results of MMDQ-codec MATLAB simulation (compare floating point with fixed point implementation)

We can see, that floating-point and fixed-point implementations are almost identical.

4.C-language implementation of MMDQ-codec

MMDQ-codec has been implemented in C-language and compiled with GCC in Linux.

5.Comparing MMDQ with G.711 and G.726 (speech)

Next tables and plots contain results of comparing G.711, G.726, MMDQ codecs. C-language implementations of these codecs has been used. Next scripts were used: demo_female.sh, demo_male.sh, demo_modem.sh, main_female.m, main_male.m, main_modem.sh.

G.711 A-law – is ITU-T standard of audio A-law companding, 64 kbits/s bit rate.
G.711 mu-law – is ITU-T standard of audio mu-law companding, 64 kbits/s bit rate.
G.726-32 – is an ITU-T ADPCM speech codec standard, 32 kbits/s bit rate.
G.726-40 – is an ITU-T ADPCM speech codec standard, 40 kbits/s bit rate.
MMDQ-32-1 is MMDQ with 32 kbits/s bit rate, spf=14, bps=3, smooth=1
MMDQ-32-2 is MMDQ with 32 kbits/s bit rate, spf=14, bps=3, smooth=2
MMDQ-32-3 is MMDQ with 32 kbits/s bit rate, spf=14, bps=3, smooth=3
MMDQ-32-4 is MMDQ with 32 kbits/s bit rate, spf=14, bps=3, smooth=4
MMDQ-40-1 is MMDQ with 40 kbits/s bit rate, spf=13, bps=4, smooth=1
MMDQ-40-2 is MMDQ with 40 kbits/s bit rate, spf=13, bps=4, smooth=2
MMDQ-40-3 is MMDQ with 40 kbits/s bit rate, spf=13, bps=4, smooth=3
MMDQ-40-4 is MMDQ with 40 kbits/s bit rate, spf=13, bps=4, smooth=4
MMDQ-40x-1 is MMDQ with 40 kbits/s bit rate, spf=7, bps=3, smooth=1
MMDQ-40x-2 is MMDQ with 40 kbits/s bit rate, spf=7, bps=3, smooth=2
MMDQ-40x-3 is MMDQ with 40 kbits/s bit rate, spf=7, bps=3, smooth=3
MMDQ-40x-4 is MMDQ with 40 kbits/s bit rate, spf=7, bps=3, smooth=4

Table 2. Comparing of codecs quality (MSE)
codec	female	male	modem (psk8)
G.711 A-law	0.00000314	0.00000113	0.000039
G.711 mu-law	0.00000326	0.00000122	0.000042
G.726-32	0.00002662	0.00001503	0.020866
G.726-40	0.00001206	0.00000737	0.003685
MMDQ-40-1	0.00002568	0.00002069	0.007104
MMDQ-40-2	0.00001642	0.00001335	0.004879
MMDQ-40-3	0.00001531	0.00001233	0.004453
MMDQ-40-4	0.00001350	0.00001052	0.003457
MMDQ-40x-1	0.00003469	0.00003176	0.010453
MMDQ-40x-2	0.00002227	0.00002191	0.008233
MMDQ-40x-3	0.00001859	0.00001810	0.006512
MMDQ-40x-4	0.00001664	0.00001520	0.005583
MMDQ-32-1	0.00010967	0.00008894	0.022521
MMDQ-32-2	0.00006535	0.00005483	0.019355
MMDQ-32-3	0.00005273	0.00004527	0.013981
MMDQ-32-4	0.00004631	0.00003948	0.013061

Figure 11. Comparing of codecs quality (MSE)

Figure 12. Comparing of codecs quality (MSE)

To evaluate codecs speed test utility with –speed option has been used (which is executed in demo_speed.sh script). It encoded/decoded 60 minutes of randomly generated sound with every codec. Results are in Table 3.

Table 3. Comparing of codecs results (speed)
codec	Encode time, ms	Decode time, ms
G.711 A-law	48	44
G.711 mu-law	48	45
G.726-32	6089	6008
G.726-40	6248	5879
MMDQ-40-1	427	404
MMDQ-40-2	1708	404
MMDQ-40-3	2331	404
MMDQ-40-4	2962	404
MMDQ-40x-1	457	430
MMDQ-40x-2	1893	430
MMDQ-40x-3	2585	430
MMDQ-40x-4	3264	430
MMDQ-32-1	395	378
MMDQ-32-2	1661	378
MMDQ-32-3	2304	378
MMDQ-32-4	2905	378

Figure 13. Comparing of codecs results (speed)

6.Modem signal transparency of MMDQ and G.726 codecs

Sometimes we need to transmit modem signal over VoIP channel (for example, FAX signal), so we need to evaluate transparency of codec we used.

Modem signal samples for random input data (16000 words) have been generated with MATLAB Communications Toolbox (main_modem_generate.m script). Then these signals were encoded/decoded and demodulated back (demo_modem.sh and main_modem.m scripts). Results are in table:

Next table shows some modems standards characteristics:

Table 4. Modem recommendations and their simulation in MATLAB
Recom-mendation	Bit rate, bit/s	Carrier frequency, Hz	Symbol rate, baud	Modula-tion	MATLAB Communications Toolbox function to model modem
-	-	-	-	-	ask2: / dmod(data,1600,1600,8000, 'ask',2)
V.21	300	1300,2100	300	FSK	-
V.23	1200	1800	1200	FSK	fsk2: / dmod(data,1600,1600,8000, 'fsk',2)
V.26	2400	1800	1200	4-DPSK	psk4: / dmod(data,1600,1600,8000, 'psk',4)
V.26 bis	2400	1800	1200	4-DPSK	-
V.27 ter	4800	1700	1600	8-DPSK	psk8: / dmod(data,1600,1600,8000, 'psk',8)
V.29	9600	1200,2400	2400	16-QAM	qask16: / dmod(data,1600,1600,8000, 'qask',16)
V.22	1200	1200,2400	600	4-DPSK	-
V.22 bis	2400	1800	600	16-QAM	-
V.32	9600	1800	2400	16-QAM	qask16: / dmod(data,1600,1600,8000, 'qask',16)
V.33	14400	1800	2400	32-QAM	qask32: / dmod(data,1600,1600,8000, 'qask',32)
V.34	28800 / 31200 / 33600		2400 / 2800 / 3000 / 3200 / 3249	16-QAM / 32-QAM / 64-QAM	qask64: / dmod(data,1600,1600,8000, 'qask',64)

Table 5. Modem transparency test (MSE)
codec	ask2	fsk2	psk4	psk8	qask16	qask32	qask64
G.711 A-law	0.000042	0.000042	0.000059	0.000039	0.000479	0.002215	0.002156
G.711 mu-law	0.000057	0.000057	0.000067	0.000042	0.000631	0.001884	0.002386
G.726-32	0.092969	0.003321	0.020406	0.020866	0.159933	0.298936	0.596903
G.726-40	0.058492	0.000843	0.005813	0.003685	0.881899	0.093240	1.187385
MMDQ-40-1	0.006580	0.005572	0.004971	0.007104	0.097918	0.273556	0.506876
MMDQ-40-2	0.005639	0.004673	0.004152	0.004879	0.063755	0.142278	0.300155
MMDQ-40-3	0.001943	0.004673	0.003384	0.004453	0.058779	0.129736	0.272807
MMDQ-40-4	0.001943	0.001094	0.003232	0.003457	0.045803	0.102590	0.220322
MMDQ-40x-1	0.012644	0.017219	0.011064	0.010453	0.153555	0.359989	0.696995
MMDQ-40x-2	0.007888	0.010049	0.007885	0.008233	0.108319	0.235181	0.484806
MMDQ-40x-3	0.006817	0.008339	0.006626	0.006512	0.092403	0.184970	0.393065
MMDQ-40x-4	0.006601	0.007958	0.006369	0.005583	0.078995	0.156969	0.308944
MMDQ-32-1	0.024533	0.028530	0.024059	0.022521	0.360753	0.839409	1.665224
MMDQ-32-2	0.013166	0.026153	0.018125	0.019355	0.247227	0.547382	1.146989
MMDQ-32-3	0.010631	0.025875	0.015140	0.013981	0.221341	0.438678	0.973957
MMDQ-32-4	0.010959	0.024819	0.014971	0.013061	0.189905	0.381230	0.807248

Table 6. Modem transparency test (absolute error rate)
codec	ask2	fsk2	psk4	psk8	qask16	qask32	qask64
G.711 A-law	0	0	0	0	0	0	0
G.711 mu-law	0	0	0	0	0	0	0
G.726-32	0	0	0	4	186	1054	2173
G.726-40	0	0	0	1	968	261	810
MMDQ-40-1	1	2	2	3	12	180	554
MMDQ-40-2	1	2	2	2	2	11	164
MMDQ-40-3	1	2	2	2	2	8	129
MMDQ-40-4	1	2	2	2	2	3	69
MMDQ-40x-1	0	0	0	4	49	562	1936
MMDQ-40x-2	0	0	0	0	5	182	1198
MMDQ-40x-3	0	0	0	0	1	62	617
MMDQ-40x-4	0	0	0	0	1	33	303
MMDQ-32-1	0	0	0	48	236	1362	3675
MMDQ-32-2	0	0	0	25	80	619	2774
MMDQ-32-3	0	0	0	2	58	384	2330
MMDQ-32-4	0	0	0	0	29	338	1895

Figure 14. Modem transparency (MSE)

Figure 15. Modem transparency (MSE)

Figure 16. Modem transparency (error rate)

Figure 17. Modem transparency (error rate)

I think, that real environment fax/DTMF transmission tests are needed, but simulation test shows, that MMDQ-codec has comparable with G.726 transparency for fax/DTMF signals.