MMDQ-codec

Content

1. Overview
2. MMDQ-codec description
3. MATLAB simulation of MMDQ-codec
4. C-language implementation of MMDQ-codec
5. Comparing MMDQ with G.711 and G.726

1.Overview

This document contains short description of Min-Max-Difference-Quantization (MMDQ) codec.

2.MMDQ-codec description

MMDQ-codec has been created as very low MIPS (CPU usage) alternative of G.726-32 (ADPCM codec with 32 kbits/sec bitrate, 8000 Hz sample rate).

Main properties of MMDQ-codec:

- Very low MIPS (CPU usage)
- Waveform lossy compression
- No restoration delay after corrupter/lost received frame (Note: G.726 has this).
- Transparancy for fax (up to ???? bod) or DTMF signals (for bitrates >= 32 kbits/sec)
- Easy adaptation to other bitrates or/and sample rates
- Algorithm simplicity

2.1. Min-Max-Differencies-Quantization Frame Format

Note: MATLAB/Octave/FreeMat array index notation is used, so index of first array element is 1 (not 0)!

Encoded data frame has next format:

MINX/MAXX
MAXX/MINX
SMOOTH-BITS[2..S]
DIFF[1..(N-1)]

Where:

MINX - minimal signal value in signal frame to be encoded (it may be encoded by A-law/mu-law encoder or by other compander method)

MINX - maximal signal value in signal frame to be encoded (it may be encoded by A-law/mu-law encoder or by other compander method)

Note: if MINX is first and MAXX is next, decoder must set SMOOTH-BIT[0]=0,
if MAXX is first and MINX is next decoder must set SMOOTH-BIT[0]=1.

S - total number of smooth bits.

SMOOTH-BITS[1..S] - array of smooth bits. Smooth bits define code of decoder function/table will be used to restore linear differencies from DIFF[] array elements.

N - number of signal samples in single frame to be encoded.

DIFF[1..(N-1)] - array of companded relative differencies between signal samples.

For example, 32 kbits/sec version of MMDQ-codec encoded data frame format is:

MINX (8 bits) - A-law companded signal value
MAXX (8 bits) - A-law companded signal value
SMOOTH-BITS (1 bit) - smooth bit number 2 (number 1 is defined by MIN/MAX order).
DIFF[1..13] (13*3=39 bits) - differencies (3 bits per difference, samples per frame is 14).

Total frame size (for 14 voice samples to be encoded) is 8+8+1+39=56 bits (7 bytes).

2.2.MMDQ Algorithm Description

Note: MATLAB/Octave/FreeMat array index notation is used, so index of first array element is 1 (not 0)!

Encoding:

1. Get sound samples X[i], i=1..N in linear format (these may be decoded A-law).
2. Find MINX, MAXX over X[i], i=1..N
3. Calculate DIFFX=MAXX-MINX
4. Calculate DX[i]=X[i+1]-X[i], i=1..(N-1)
5. Get AMPDX = max(abs(DX[i])), i=1..(N-1) - maximum amplitude of DX[i].
6. For every difference companding function DV[s]=F[s](DX), s=1..SMOOTH_N calculate maximum reconstruction error ERR[s]:

6.1. Get DV[s][i]=F[s](DX[i]), i=1..(N-1)
Note: different companding functions F[s](DX) are used to minimize encode/decode reconstruction error.

Default F[s](DX) is linear function:
F[s](DX)=DX

6.2. Quantize DV[i] into DIFF[i] values. Here i=1..(N-1). If encoder use
        BITS bits per difference, then DIFF[i] will be of range [0..(FACTOR-1)],
        where FACTOR=2^BITS.
        Approximate quantization function is: DIFF[i]=FACTOR*DV[i]/AMPDX + FACTOR/2,
        where i=1..(N-1).

        Note special case: AMPDX==0

6.2. Prepare data_frame[s] for MINX, MAXX, SMOOTH==s, DIFF[s][i], i=1..(N-1)

        Note: if SMOOTH(bit0)==0, put MINX first, MAXX second.
        If SMOOTH(bit0)==1, put MAXX first, MINX second.

6.3. Decode data_frame[s] into sound waveform: Y[s][i], i=1..N

6.4. Calculate ERR[s]=max(abs(X[i]-Y[s][i])), i=1..N

7.Find MINERR=min(ERR[s]), s=1..SMOOTH_N. Let's s0 - SMOOTH for
data_frame with best (minimal) reconstruction error: ERR[s0]=MINERR.

8.Ouput data_frame[s0].

--------------------------------------------------------------------------------

Decoding:

1.Get encoded data: data_frame=B[k], k=1..M (M-total size of data, bits).

2.Get MINX, MAXX, SMOOTH_BIT[1..s], DIFF[1..(N-1)] from data_frame.
For example, for 32 kbits/sec 8000 Hz format:

M1=B[1..8]
M2=B[9..16]
if M1<=M2
    SMOOTH_BIT[1]=0
    MINX=M1
    MAXX=M2
else
    SMOOTH_BIT[1]=1
    MINX=M2
    MAXX=M1
end
SMOOTH_BIT[2]=B[17]
i=1
k=18
while(k<=M)
    DIFF[i]=B[k..k+2]
    i=i+1
    k=k+3
end

3.Calculate used smooth: s0=SMOOTH_BIT[1..s]

4.Calculate DIFFX=MAXX-MINXX

5.Calculate first estimation of sound samples values:
Y[1]=0
for i=2:N
    DY = R[s0]( 2*DIFF[i-1]/FACTOR - 1 )
    Y[i] = Y[i-1] + DY
end

Where DY=R[s](DIFF) is difference decompanding function for defined smooth s0.
This function is inverse for DIFF=F[s](DY).

6.Find MINY, MAXY over Y[i], i=1..N.

7.Calculate DIFFY=MAXY-MINY

8.Scale and shift Y[i], i=1..N to the range [MINX..MAXX] by formula:

for i=1:N
    Y[i] = DIFFX * ( Y[i]-MINY ) / DIFFY + MINX
end

Note special case: DIFFY==0

3.MATLAB simulation of MMDQ-codec

4.C-language implementation of MMDQ-codec

5.Comparing MMDQ with G.711 and G.726